## Slide 1
Smart Water Intelligence
Real-Time Monitoring & Adaptive Leak Protection
ESP32
MQTT
Node-RED
CFAD

## Slide 2
System Architecture
End-to-end IoT pipeline from sensor to intelligence
Physical Layer
YF-S401 Sensor
12V NC Valve
ESP32-WROOM
Edge Device
MQTT
Message Broker
Mosquitto MQTT
Port 1883
QoS 0/1/2
Local Network
JSON
Logic Engine
Node-RED Flows
CFAD Algorithm
Adaptive Thresholds
Processing
HTTPS
User Interface
Dashboard UI
Telegram Bot
CSV Logging
Presentation
water/flow
L/min
water/valve
0/1
alerts
JSON

## Slide 3
Hardware Stack
Industrial-grade components with fail-safe design
GPIO 27/26
ESP32-WROOM
Dual-core controller with Wi-Fi & MQTT client. Handles interrupts, OLED display, and relay control.
802.11 b/g/n
5V Logic
YF-S401
Flow Sensor
Hall-effect sensor with 1/8" NPT threads. Detects 0.3–6 L/min with pulse output.
7.5 pulses/L
5V DC
12V NC
Solenoid Valve
Normally-closed 2-way valve. Fail-safe design—closes on power loss or leak detection.
Fail-Safe NC
<50ms response
5V Opto
Relay Module
Opto-isolated 1-channel relay. Switches 12V valve safely from 3.3V ESP32 logic.
10A @ 250VAC
Isolation
XY-3606
Power Management
12V→5V buck converter powers ESP32, sensors, and relay. 2A supply with common ground.
12V 2A Input
5V 5A Output
I2C
OLED Display
0.96" SSD1306 local display. Shows live flow, WiFi status, and valve state independent of cloud.
128×64px
SDA/SCL

## Slide 4
Continuous Flow Anomaly Detection
Self-learning algorithms for intelligent water management
Adaptive Thresholds
System learns 7-day average usage and dynamically adjusts leak threshold (avg/10, clamped 3-10 L/min). Eliminates false alarms for different building types.
Micro-Leak Detection
Detects continuous low flow (>0.5 L/min) for 2+ hours. Catches dripping taps and silent pipe leaks that high-threshold systems miss.
Spike Detection
Triggers when flow increases 3× within 2 seconds. Identifies burst pipes or sudden pressure failures for immediate shutoff.
Predictive Analytics
Calculates monthly usage projection based on rolling 7-day average. Estimates water bills at ₹15 per 1000L.
Formula:
prediction = avg_daily × 30
Efficiency Scoring
0-100 score based on daily budget (150L). Penalizes over-usage (-20 pts) and warns at 80% threshold (-10 pts). Gamifies conservation.
Night Anomaly
Monitors 2AM–4AM window. Any flow >1 L/min during sleep hours triggers immediate alert—catches illegal usage or hidden leaks.

## Slide 5
Live System & Impact
Real-time protection with zero-latency response
Node-RED Dashboard
Flow Rate
7.2
L/min
System Status
Leak Detected
Valve auto-closed • Telegram sent
Efficiency Score
72
/100
Moderate Usage
Monthly Prediction
₹1,245
Est. 2,490L usage
Telegram Alerts
⚠ Leak detected!
Flow: 7.2 L/min
Valve closed
Key Metrics
Response Time
<1s
False Alarms
0%
Data Logging
CSV
Protocol
MQTT
Smart
Water Intelligence